## Slide 1: Introducing RC’s new NVIDIA Grace Hopper Superchip

## Slide 2: Introducing RC’s new NVIDIA Grace Hopper Superchip
Instructor: Brandon Reyes
  Research Computing
Website: www.rc.colorado.edu
Documentation: https://curc.readthedocs.io
Helpdesk: rc-help@colorado.edu
Survey: http://tinyurl.com/curc-survey18

## Slide 3
Meet the User Support Team
Layla Freeborn
Brandon Reyes
Andy Monaghan
Michael Schneider
John
Reiland
Dylan Gottlieb
Mohal Khandelwal
Ragan
Lee

## Slide 4
Slides https://github.com/ResearchComputing/introducing_rc_gh200_quick_byte

## Slide 5: Session Overview
GH200 architecture overview
  Hardware specs
What workflows will benefit from the GH200 architecture?
RC’s approach to software management
Beta testing phase
How can you run on the GH200s?

## Slide 6: GH200 architecture overview
The Grace Hopper Superchip (GH200) is a newer chip provided by NVIDIA that allows the Grace CPU and Hopper GPU to concurrently and transparently access both the CPU and GPU memory
Image provided by https://resources.nvidia.com/en-us-grace-cpu/nvidia-grace-hopper

## Slide 7: Specifications for our 2 GH200 nodes
Grace CPU has 72 cores and roughly 480 GB of RAM
  Arm based (Neoverse V2)
Hopper GPU is an H100 and has roughly 100 GB of VRAM
CPU and GPU are connected via NVIDIA NVLink-C2C
FAST I/O speed (512 GB/s)
  Top I/O speeds only apply to the SSD
Roughly 1.7 TB of usable SSD on the node
Note: We have not enabled linking of multiple GH200 nodes

## Slide 8: Benefits of GH200 architecture
NVLink-C2C provides seamless memory management between the CPU and GPU
  Allows GPU threads to access RAM, extending the GPU memory
1:1 GPU-to-CPU ratio
  GPU and CPU have roughly the same processing power dedicated to them
  Ideal for workloads that utilize the CPU and GPU to a high degree
High-speed I/O to SSD and large SSD storage space
  Allows users to store a large amount of their data locally on the node (while it is in use) and quickly access it

## Slide 9: What workflows will benefit from the GH200 architecture?
Heterogenous software that uses both the CPU and GPU
Inference for Large Language Models
  I was able to run Llama 3.1 405b (requires close to 300 GB of memory)
Training large models and hyperparameter tuning
  We have seen at least 2X speedup, some users reported 10X speedup
NVIDIA also states that the following applications perform well on the GH200s:
  Graph Neural Networks, ABINIT, OpenFOAM, GROMACS, FFTs, Multi-Grid Linear Solvers

## Slide 10: RC’s approach to software management
Due to the different architecture, there is a limited software stack. We currently provide:
CUDA compilers through NVIDIA HPC SDK e.g. nvcc, nvc++
CUDNN libraries
Miniforge (mamba and conda)
  If your specific library allows for aarch64 architecture with GPU capabilities, it will most likely work on the GH200s
Apptainer
  A large selection of compatible containers are available through NVIDIA’s NGC catalog
We will work with you to install GH200 compatible software, in alignment with our software polices.

## Slide 11: Beta testing phase
To identify issues and workflows that best run on the GH200s, we initiated a beta testing phase.
This is directed towards users with established GPU workflows on either our A100 or MI100 GPUs
An initial consultation is held to determine if the workflow is appropriate for the GH200s
Once approved, we setup the software on the GH200s, onboard you to the nodes, and provide hands-on support for any issues encountered

## Slide 12: How can you run on the GH200s?
Submit a ticket to rc-help@colorado.edu
  In subject include:
    You are interested in running “X application” on the GH200s
  In the email body:
    Short description of what your workflow is trying to accomplish
    Why you believe the GH200s would be beneficial to your workflow
    Provide us Linux paths to the code you would like to run
    If possible, any JobIDs of this workflow you have ran on a GPU node

## Slide 13: Thank you!
http://tinyurl.com/curc-survey18
Survey and feedback

## Slide 14
Slides https://github.com/ResearchComputing/introducing_rc_gh200_quick_byte